## Slide 1: 唤醒流程分析 LCM和HDMI唤醒问题分析

## Slide 2: Outline
Display唤醒流程
Log分析
实例

## Slide 3
说明：请优先参看“唤醒流程分析——Framework PowerMS分析过程”这篇ecourse，定位按下Power key后哪个阶段出现问题，定位为display这边出现问题，再根据该ppt分析

## Slide 4: Display唤醒流程
由PowerManagerService 逐步对display、tvout(如果支持)、HDMI进行唤醒。
alps/frameworks/base/services/java/com/android/server/power/ PowerManagerService.java
唤醒display
唤醒HDMI

## Slide 5: Kernel 对应流程
由linux early suspend和late resume机制叫醒LCM
Display睡眠对应call到mtkfb.c中mtkfb_early_suspend
Display唤醒对应call到mtkfb.c中mtkfb_late_resume
alps/mediatek/kernel/drivers/video/mtkfb.c
Enter late _resuem
DISP_PowerEnable(TRUE)
DISP_PanelEnable(TRUE)
Set_backlight_level
Leave late_resume
set backlight off
Enter early_suspend
DISP_PanelEnable(FALSE)
DISP_PowerEnable(FALSE)
Leave early_suspend
mtkfb_early_suspend
mtkfb_late_resume
lcm_suspend
lcm_resume

## Slide 6: Kernel LOG分析
<5>[ 298.502758] (0)[25:pmic_thread_kth][Power/PMIC] [pwrkey_int_handler] Release pwrkey
<4>[ 298.503878] (0)[25:pmic_thread_kth]kpd: Power Key generate, pressed=0
<4>[ 298.623509] (0)[1588:kworker/u:4][FB Driver] enter late_resume
<4>[ 298.988860] (1)[1588:kworker/u:4][FB Driver] leave late_resume
<4>[ 299.135471] (1)[577:PowerManagerSer][HDMI] hdmi ioctl= MTK_HDMI_POWER_ENABLE(12), arg = 1
<4>[ 299.573068] (1)[577:PowerManagerSer][hdmi_drv]hdmi_drv_get_state,773 sii status:0
<4>[ 299.574113] (1)[577:PowerManagerSer][wfd]hdmi_ioctl,#1182 [HDMI] hdmi ioctl= MTK_HDMI_POWER_ENABLE(12)
<4>[ 299.581339] (3)[577:PowerManagerSer]mt65xx_leds_set_cust: set brightness, name:lcd-backlight, mode:6, level:102
按下power key
LCM resume时间
HDMI resume时间
背光开启
整个流程耗时：1.077s
其中LCM resume时间365ms
HDMI resume时间440ms

## Slide 7
1、Power key 到[FB Driver] enter late_resume之间耗时较长
以及
[FB Driver] leave late_resume到hdmi ioctl= MTK_HDMI_POWER_ENABLE(12)之间耗时较长
请参考“唤醒流程分析——psensor唤醒及backlight控制问题分析”ecourse 分析
2、[FB Driver] enter late_resume到[FB Driver] leave late_resume之间耗时较长
1）查看是否有error的耗时log打出，如DSI busy等信息。
2）如没有异常，查看LCM driver是否本身resume函数时间就较长，如调用initial code，其间有长时间delay等等
3、HDMI power enable之间耗时较长
1）请查看hdmi driver中是否有额外delay
2）查看hdmi流程是否有哪个环节耗时额外过程，请提交eservice并附上对应log过来，一起分析

## Slide 8: 实例1
<4>[21019.466194] (0)[25:pmic_thread_kth]kpd: Power Key generate, pressed=0
<4>[21019.588399] (0)[1558:kworker/u:3][FB Driver] enter late_resume
<4>[21019.802770] (0)[1558:kworker/u:3][FB Driver] leave late_resume
<4>[21019.860498] (1)[643:PowerManagerSer][hdmi]hdmi_ioctl,#2450 [HDMI] hdmi ioctl= MTK_HDMI_POWER_ENABLE(12), arg = 1
<4>[21020.464055] (1)[643:PowerManagerSer][hdmi_drv]hdmi_drv_get_state,789 sii status:0
<4>[21020.465101] (1)[643:PowerManagerSer][wfd]hdmi_ioctl,#1135 [HDMI] hdmi ioctl= MTK_HDMI_POWER_ENABLE(12)
<4>[21020.488992] (0)[643:PowerManagerSer]mt65xx_leds_set_cust: set brightness, name:lcd-backlight, mode:6, level:212
整个流程耗时：1.02s
其中LCM resume时间214ms
HDMI resume时间604ms
整个流程都是OK的，HDMI power enable的时间
相对较长，查看发现，其hdmi_drv.c中
power enable函数有额外添加delay(150ms)
再reset(55ms)左右等

## Slide 9
实例2
<4>[ 401.608020] (0)[25:pmic_thread_kth]kpd: Power Key generate, pressed=1
<4>[ 401.695405] (0)[43:kworker/u:1][FB Driver] enter late_resume
<4>[ 403.902596] (1)[43:kworker/u:1][FB Driver] leave late_resume  2.3s LCM才唤醒
<4>[ 404.065473] (1)[567:PowerManagerSer]mt65xx_leds_set_cust: set brightness, name:lcd-backlight, mode:5, level:255
<4>[ 403.867066] (2)[43:kworker/u:1][DISP/DSI] Wait for DSI engine not busy timeout!!!
<5>[ 403.868009] (2)[43:kworker/u:1][DISP/DSI] ---------- Start dump DSI registers ----------
<5>[ 403.869017] (2)[43:kworker/u:1][DISP/DSI] DSI+0000 : 0x00000001
<5>[ 403.869755] (2)[43:kworker/u:1][DISP/DSI] DSI+0004 : 0x00000000
……
<5>[ 403.901502] (1)[43:kworker/u:1][DISP/DSI] DSI_CMD+0000(f400d180) : 0x00290508
<5>[ 403.901524] (1)[43:kworker/u:1][DISP/DSI] DSI_CMD+0004(f400d184) : 0x0300002b
<5>[ 403.901547] (1)[43:kworker/u:1][DISP/DSI] DSI_CMD+0008(f400d188) : 0x000000bf
LCM resume之间有如下log，表明DSI出现异常 (timeout时间为2s)
该处的异常发生在LCM resume的流程之中，先检测LCM driver，如上cmdq中有00290508这样的序列
检测LCM driver，为cmd mode，而在lcm_update函数中并未注释掉如下code：
data_array[0]= 0x00290508;
dsi_set_cmdq(data_array, 1, 1);
在89后，最新的LCM porting guard有介绍该code需要拿掉
修后测试OK

## Slide 10
实例3
项目一 kernel log:
<4>[51936.187632] (1)[25:pmic_thread_kth]kpd: Power Key generate, pressed=1
<4>[51936.231851] (2)[6546:kworker/u:5][FB Driver] enter late_resume
<4>[51936.642981] (0)[6546:kworker/u:5][FB Driver] leave late_resume  LCM 唤醒411ms
<4>[51936.713164] (1)[588:AALServiceMain]mt65xx_leds_set_cust: set brightness, name:lcd-backlight, mode:6, level:30
 一共唤醒时间525ms
项目二 kernel log:
<4>[88157.168031] (1)[25:pmic_thread_kth]kpd: Power Key generate, pressed=1
<4>[88157.279519] (1)[5250:kworker/u:5][FB Driver] enter late_resume
<4>[88157.956199] (0)[5250:kworker/u:5][FB Driver] leave late_resume LCM 唤醒677ms
<4>[88158.058818] (2)[599:PowerManagerSer]mt65xx_leds_set_cust: set brightness, name:lcd-backlight, mode:6, level:30
 一共唤醒时间891ms
项目二中，lcm resume中是通过去call lcm init函数，而在lcm init函数中有很长的cmd发送。还有200ms的delay。
89以后的平台cmd mode和video mode都是可以在LCM suspend的时候不需要去拉reset，resume的时候无需重新init，
说明：resume的时间需要在use mode下测试，
不同项目可能时间会有差异，该例子时间不作为官方参考

## Slide 11: Thanks